## Slide 1: Manager guidelines for safe lifting
Clear spaces to improve access to materials or products being handled.
Reduce frequency, intensity and time employees perform lifting/carrying tasks.
Minimize the distances loads are lifted, raised/lowered and transported.
Position storage shelves at heights between 15” – 40” for heavier items.
Do not position lift aids lower than 15” to discourage lifting below the knees.
Avoid storing items on the ground to eliminate lifting from the floor level.
Plan a safe workflow and workspace
Respect the power zone
Tag the load to alert workers.
Test the load for stability and weight before carrying the load.
Reduce the weight of the load.
Repack containers to balance weight.
Implement lifting aids such as carts, lift tables, pallet jacks or forklifts.
Position delivery vehicles close to docks.
Use a team of people to lift/carry.
Submit a Move Request.
Lift heavy, unstable loads with care
Use aids and resources for safe lifting

## Slide 2: Employee guidelines for safe lifting
Check for tags and labels on loads.
Test the load for stability and weight.
Ensure shoes and gloves fit securely for optimal strength, stability, and grip.
Lift and carry from your power zone: the area above the knees, below the shoulders, and close to the body.
Use a stepstool or lift aid to adjust.
If you must lift from the floor, do not bend at the waist.
Do a pre-lift inspection
Remember your power zone
Get a secure grip with both hands.
Move smoothly and evenly, without jerking or twisting.
Use your legs to push up and lift.
Take rest breaks.
Use a cart, pneumatic/electric lift table, pallet jack, or forklift to assist you.
Repack containers to lighten or stabilize.
Ask your team for assistance.
Submit a Move Request.
Lift with confidence
Take care with unstable, heavy loads